## Slide 1: 2010 Standards for Accessible Design
Presented By: Michael A. Edwards Great Plains ADA Center

## Slide 2: Update on DOJ’s ADA Standards
DOJ – Published as a Standard
Sept, 15 2010
Effective Date:
For all New and altered facilities
March 15, 2012

## Slide 3: Department of Justice ADA Standards
The Department of Justice (DOJ) published updated ADA regulations based on the Access Board's guidelines.
These regulations include additional design requirements that supplement the standards.

## Slide 4: Update on DOJ’s ADA Standards

## Slide 5: Safe Harbor and the 2010 SAD
If elements in an existing facility have not been altered on or after March 15, 2012, and these elements comply with the corresponding technical and scoping specifications in the 1991 Standards, they are not required to be modified in order to comply with the requirements set forth in the 2010 ADA Standards.

## Slide 6: Safe Harbor and the 2010 SAD
Chapter 10 of the 2010 SAD did not exist.
Except where noted – Boating Facilities – every topic of Chapter 10 would be required to be made accessible now.
For Title II, this means a review of Program Access.
For Title III, this means RABR.

## Slide 7: Elements in 2010 Standards not Subject to Safe Harbor
(A) Residential facilities dwelling units
(B) Amusement rides
(C) Recreational boating facilities
(D) Exercise machines and equipment
(E) Fishing piers and platforms
(F) Golf facilities
(G) Miniature golf facilities

## Slide 8: Elements in 2010 Standards not Subject to Safe Harbor
(H) Play areas
(I) Saunas and steam rooms
(J) Swimming pools, wading pools, and spas,
(K) Shooting facilities with firing positions,
(L) Miscellaneous.
(1) Team or player seating
(2) Accessible route to bowling lanes
(3) Accessible route in court sports facilities

## Slide 9: Path of Travel - Safe Harbor
If a covered entity has constructed or altered required elements of a path of travel in compliance with the applicable Standards (1991 or UFAS), before March 15, 2012, they are not required to retrofit such elements to reflect incremental changes in the 2010 Standards, just because they alter a primary function area served by the path of travel.

## Slide 10: Updated ADAAG
Application and
General Scoping

## Slide 11: New Format
Numbering system
New figures (informational only)
All dimensions in text
(not just figures)
New advisory notes follow provision

## Slide 12: ADAAG Supplements
Previous supplements included:
State & Local Gov’t Facilities (1998)
Children’s Environments (1998)
Play Areas (2000)
Recreation Facilities (2002)

## Slide 13: Harmonization
ICC/ANSI A117.1-2003 IBC 2003

## Slide 14: Significant Changes to ICC/A117.1 2015
Anthropometric Changes to:
turning radius
Clear Floor Space
New Dimensions mentioned throughout PowerPoint

## Slide 15: CHAPTER 1
Application and Administration
101 – Purpose
102 – Dimensions for Adults and Children
103 – Equivalent Facilitation
104 – Conventions
105 – Referenced Standards
106 – Definitions

## Slide 16: Conventions
Dimensions – range instead of absolute dimension where possible
Construction and manufacturing tolerances
Calculation of percentages
Figures – informational; text governs

## Slide 17: Ranges instead of absolute dimensions
Water closet centerline (16-18”)
Width of ambulatory accessible stall (35”- 37”)

## Slide 18: Some absolute dimensions remain
Transfer shower stall (36” x 36”) and combination transfer/roll-in design with seat on front wall (36” deep)
measured to center points; manufacturing tolerances recognized

## Slide 19: Referenced Standards
powered doors (ANSI/BHMA A156.10 & A156.19)
elevators and lifts (ASME A17.1 & A18.1)
egress (IBC)
alarms (NFPA 72)
play surfacing & equipment (ASTM standards)

## Slide 20: Adult and Children’s Dimensions
Anthropometrics drive the design
New children's guidance covers:
  Drinking fountains
  Water closets
  Toilet compartments
  Lavs/sinks
  Dining and work surfaces

## Slide 21: Equivalent Facilitation
103 Equivalent Facilitation
Nothing in these requirements prevents the use of designs, products, or technologies as alternatives to those prescribed, provided they result in substantially equivalent or greater accessibility and usability.

## Slide 22: CHAPTER 2 General Scoping and Exceptions

## Slide 23: Application (201)
Premise:
All areas of newly designed/ constructed facilities to comply unless indicated
Exceptions more thoroughly covered

## Slide 24: Temporary and Permanent Structures
201.3 – Regulations apply to both
Classrooms
Bleachers
Stages
Platforms/daises
Exhibits
NOT Construction

## Slide 25: Existing Buildings and Facilities (202)
Additions
Alterations
(specific exceptions now located at relevant provision)
Primary Function Areas – Path of Travel
Qualified Historic Facilities

## Slide 26: 202- Additions, Alterations, Usability
Additions comply with the provisions for new construction
  Usability must be considered
Alterations: Redefined.
  Usability must be considered
  Path of travel and 20% non-proportionality

## Slide 27: Alterations
TECHNICAL INFEASIBILITY
In alterations, where compliance with applicable requirements is technically infeasible, the alteration shall comply with the requirements to the maximum extent feasible.

## Slide 28: Alterations: Primary Function Areas
202.4 Alterations Affecting Primary Function Areas.
An alteration that affects or could affect the usability of or access to an area containing a primary function shall be made so the path of travel to the altered area is readily accessible to and usable by individuals with disabilities
  unless such alterations are disproportionate to the overall alterations in terms of cost and scope

## Slide 29: Alterations – Path of Travel
20% OF ALTERATION TO PRIMARY FUNCTION AREA
INCLUDES ROUTE AND
  Restrooms
  Telephones
  Drinking fountains

## Slide 30: ALTERATIONS – PRIMARY FUNCTION AREA
EXAMPLES OF AREAS INCLUDED: EMPLOYEE WORK AREAS, PUBLIC AREAS, LOBBIES, ETC.
EXAMPLES OF AREAS NOT INCLULDED:
  MECHANCIAL, BOILER, OR SUPPLY ROOMS
  EMPLOYEE LOUNGES OR LOCKER ROOMS
  ENTRANCES OR CORRIDORS
  RESTROOMS

## Slide 31: General Exceptions (203)
Sites, buildings, facilities and elements are exempt from these requirements…
Construction sites
Raised areas
Limited access spaces
Machinery spaces

## Slide 32: General Exceptions (203)
Single occupant structures (e.g., toll booths)
Certain common use spaces in detention and correction facilities and residential facilities
Employee work areas
Various spaces in recreation facilities

## Slide 33: Raised Areas
Exempt: areas raised for security, life/fire safety

## Slide 34: General Exceptions (203)
Raised referee judging and scoring areas
Water Slides
Animal containment areas
Raised boxing, wrestling rings
Diving boards and platforms

## Slide 35: Operable Parts 205
When located on accessible elements, routes and rooms, comply with 309
EXCEPTIONS:
When intended for maintenance personnel, etc.
Dedicated electrical, communication &
floor receptacles
HVAC diffusers
Redundant controls
Exercise equipment

## Slide 36: Accessible Routes (206)
Where required:
  Site arrival points
  Within sites
  (not req’d if no pedestrian route provided)
  Between stories (elevator exceptions)
  Space and elements
  Specific spaces (e.g., restaurant &
  cafeteria, performance area, press box)

## Slide 37: Accessible Routes (206)
At least one route from parking and passenger loading, public streets and sidewalks and public transportation stops to:
  The accessible building or facility entrance they serve,
  Except:
  Historic structures from site arrival point to entrance
  If the only means of access is vehicular not providing a pedestrian route

## Slide 38: Vertical access
2nd floor vs. less than 3,000 sq. ft. aggregate
  Not allowed for doctor’s offices, malls, transportation facilities
Title II buildings – two stories and above.
Title III buildings – Three stories and Sq. footage combined.

## Slide 39: Accessible Routes in multi story buildings -206.2.3
At least one route connecting stories and mezz
  Except:
  Private buildings 3000 S>F, less than 3 stories
    Except in: Shopping centers,
    malls,
    office of health care providers,
    terminals ,depots or stations for public transportation

## Slide 40: Accessible Routes in multi story buildings -206.2.3
Public (Title II) buildings exceptions:
  Two stories, with an occupant load of 5 or fewer on one level.
  Certain detention and correction facilities
  Certain residential applications
  Certain transient lodging applications
  Air traffic control towers
  Historic structures in some applications

## Slide 41: ADA Definition of Mezzanine
Mezzanine. An intermediate level or levels between the floor and ceiling of any story with an aggregate floor area of not more than one-third of the area of the room or space in which the level or levels are located.
Mezzanines have sufficient elevation that space for human occupancy can be provided on the floor below.

## Slide 42: ADA Work Areas
“approach, entry,
& exit”
circulation paths (in areas ≥ 1000 sq ft)
means of egress
visual alarm
connection

## Slide 43: Chapter 3 Building Blocks

## Slide 44: Building Blocks (Chapter 3)
Floor or Ground Surfaces
Changes in Level
Turning Space
Clear Floor/ Ground Space
Knee & Toe Clearance
Protruding Objects
Reach Ranges
Operable Parts

## Slide 45: Anthropometrics

## Slide 46: ICC Changes

## Slide 47: Turning Space (304)
clarification:
overlap of turning space where knee/ toe clearance provided
doors can swing into turning space

## Slide 48: Turning Space (304)
60 inches

## Slide 49: Turning Space (304)
Overlap permitted for only one arm of T-shaped space

## Slide 50: ICC Changes

## Slide 51: ICC Changes

## Slide 52: Knee Space (306)

## Slide 53: Toe Space (306)

## Slide 54: Reach Ranges (308)
Max. Reach – 48” Min. Reach – 15” (forward & side)

## Slide 55: Protruding Objects
Figure 307.2 Limits of Protruding Objects

## Slide 56: Figure 307.4 Vertical Clearance

## Slide 57: Operable Parts
A clear floor or ground space complying with 305 shall be provided.
Operable parts shall be placed within one or more of the reach ranges specified in 308.
Operable parts shall be operable with one hand and shall not require tight grasping, pinching, or twisting of the wrist.
The force required to activate operable parts shall be 5 pounds maximum.

## Slide 58: Accessible Routes (Chapter 4)
Accessible Route Components
  walking surfaces
  doors, doorways, gates
  ramps
  curb ramps
  elevators
  limited use/ limited application elevators
  private residence elevators
  platform lifts

## Slide 59: Performing Areas
“School board OKs stage ramps”

## Slide 60: Entrances
At least 60% of public entrances to comply
Route to entrances to coincide with general circulation routes to maximum extent feasible

## Slide 61: Walking Surfaces (403)
(Portions of accessible routes that slope no more than 1:20)
  Minimum separation (48”) between reduced clear widths
  Handrails along walking surfaces req’d to comply

## Slide 62: Slope
Cross Slope should never exceed 1:48 (2%)
Running Slope never to exceed 1:20 (5%)
  Any slope greater than 1:20 is a ramp.

## Slide 63: Doors - Clearances
Pullside clearance, forward approach
Clearance at doors in thick walls or that are recessed (8” max. offset)

## Slide 64: Doors – Clearances
Pushside clearance required at doors with a closer & latch

## Slide 65: ICC Changes

## Slide 66: Door and Gate Hardware
Handles, pulls, latches, locks, and other operable parts on doors and gates shall comply with 309.4. (Operable Parts)
Hardware shall be 34 inches minimum and 48 inches maximum above the finish floor or ground.
Where sliding doors are in the fully open position, operating hardware shall be exposed and usable from both sides.

## Slide 67: Door or Gate Hardware
NO tight grasping, pinching, or twisting of the wrist.

## Slide 68: Thresholds at doorways
Thresholds, if provided at doorways, shall be 1/2 inch high maximum.
Raised thresholds and changes in level at doorways shall comply with 302 and 303.
EXCEPTION: Existing or altered thresholds 3/4 inch high maximum that have a beveled edge on each side with a slope not steeper than 1:2 shall not be required to comply with 404.2.5.

## Slide 69: Doors in Series
New version allows both sets of doors to swing into space (with proper separation)

## Slide 70: Doors in Series
Where doors are automated, provide wheelchair space at controls outside door swing

## Slide 71: Entrances
Automated openers recommended for exterior doors
Required for Federal GSA buildings

## Slide 72: Automatic & Power Assisted Doors & Gates (404.3)
Industry standards referenced:
Full-powered: ANSI/BHMA A156.10 (1999)
Low-energy and power-assisted: ANSI/BHMA A156.19 (1997 or 2002)
New provisions for break-out opening, clear floor space at controls

## Slide 73: Automatic Doors: Clear Floor Space at Controls (404.3.5)
The clear floor space adjacent to the control shall be located beyond the arc of the door swing.
30” X 48” and on an accessible route

## Slide 74: Ramps (405)
Slope:
  1: 12 max
Handrails (> 6” rise)
  both sides
  12” extensions
  34” to 38” height

## Slide 75: Ramps (405)
Level landings (1:48 max.)
Edge protection (clarified specs)
Exceptions for ramps in work areas (width, handrails)

## Slide 76: Ramps - Edge Protection
Edge protection complying with 405.9.1 or 405.9.2 shall be provided on each side of ramp runs and at each side of ramp landings.
405.9.1 Extended Floor or Ground Surface. The floor or ground surface of the ramp run or landing shall extend 12” minimum beyond the inside face of a handrail complying with 505.

## Slide 77: Ramps - Edge Protection
Edge protection complying with 405.9.1 or 405.9.2 shall be provided on each side of ramp runs and at each side of ramp landings.
405.9.2 Curb or Barrier. A curb or barrier shall be provided that prevents the passage of a 4 inch diameter sphere, where any portion of the sphere is within 4 inches (100 mm) of the finish floor or ground surface.

## Slide 78: Curb Ramps
Smooth transition
Side flares or returned sides
Landing space (top and bottom)
Diagonal ramps discouraged
Detectable warnings

## Slide 79: Curb Ramps
side flares returned sides

## Slide 80: Curb Ramps
Bottom 4’ landing must be within crosswalk

## Slide 81: Detectable warnings
Curb ramps
On sites – no
Transit facilities - yes
Rulemaking on public rights-of-way developing more specific guidance

## Slide 82: Platform Lifts (206.7)
Alterations – no restrictions
New Construction – restricted to:
  performance areas and speaker’s platforms
  wheelchair spaces
  incidental spaces
  existing site constraints (exterior)
  other

## Slide 83: General Site & Building Elements (Chapter 5)
Parking
Passenger Loading Zones
Stairways
Handrails

## Slide 84: Parking spaces – 208
Applies to parking structures, lots. Calculated
separately in each facility.
1 to 25-1
26 to 50 -2
51 to 75 -3
76 to 100- 4
101 to 150 -5
151 to 200 -6
201 to 300 -7
301 to 400 -8
401 to 500 -9
501 to 1000 -2 percent of total
1001 and over 20, plus 1 for each 100, or fraction thereof

## Slide 85: Parking (208)
Exception - spaces used exclusively for:
Bus, trucks, and other delivery vehicles
Law enforcement vehicles
Vehicular impound
These lots must have compliant passenger loading zone where public access is provided

## Slide 86: Van Parking (208.2.4)
Van Spaces - 1 of every 6 accessible spaces (instead of 1 of 8)

## Slide 87: Van Spaces (502)
8’
EX: Van space
Car space
Van space

## Slide 88: Parking (502)
Marking of access aisles
Angled vans spaces (aisle on passenger side)
Sign height (60” min.)

## Slide 89: Parking Spaces (502)
Identification
Signs shall include the International Symbol of Accessibility
van spaces shall contain the designation "van accessible.“
60” min above the finish floor or ground surface measured to the bottom of the sign.
Relationship to Accessible Routes Parking spaces and access aisles shall be designed so that cars and vans, when parked, cannot obstruct the required clear width of adjacent accessible routes.

## Slide 90: Passenger Loading Zones (209)
At least 1 for every 100 linear ft. of loading zone space provided

## Slide 91: Passenger Loading Zones
Aisles - same level as pull-up space
Aisles to be marked
No level changes in space or aisle

## Slide 92: Handrails (505)
Handrail/ surface clearance: 1 ½” min. (not absolute)
Diameter: 1 ¼” – 2” (not 1 ½” max.)
Dimension applies to outer diameter (clarification)

## Slide 93: Handrail Gripping Surface (505.6)
Continuous gripping surface
No obstructions on top or sides
Obstructions limited along bottom to 20%
1.5” min at bottom

## Slide 94: Handrails (505.7)
gripping surface – more detail, more options
criteria for circular & non-circular cross sections

## Slide 95: Plumbing Elements & Facilities (Chapter 6)
Drinking Fountains
Toilet & Bathing Rooms
Water Closets & Toilet Compartments
Urinals
Lavatories & Sinks
Bathtubs
Shower Compartments
Grab Bars
Seats
Washing Machines & Clothes Dryers
Saunas & Steam Rooms

## Slide 96: Drinking Fountains (211)
Where provided on an exterior site or floor,
2 required: wheelchair accessible & standing access
alternative: single unit with
dual access (e.g., “hi-lo” units)
multiple installations:
50% of each type

## Slide 97: Toilet & Bathing Facilities (213)
Scoping for rooms & elements (e.g., toilets, lavs, mirrors)
toilet rooms clustered
at 1 location: 50% scoping
unisex toilet rooms
Urinals - access where
more than 1 provided

## Slide 98: Toilet Rooms & Water Closets (603 & 604)
Range for toilet centerline
lavatory cannot overlap toilet clearance (except in dwelling units)

## Slide 99: Toilet Rooms & Water Closets (603 & 604)
a fixture can be recessed
shorter (24” min.) rear grab bar allowed

## Slide 100: Toilet & Bathing Rooms (603)
Space for side transfers provided

## Slide 101: Toilet & Bathing Rooms (603)
Door can swing into fixture clearances if clear floor space provided beyond door swing

## Slide 102: Water Closets (604)
Other changes/ clarifications:
objects permitted to overlap clearance (grab bars, dispensers, etc.)
flush controls (standard reach range)
toilet paper dispenser location

## Slide 103: Water Closets (604)
revised location for toilet paper dispenser

## Slide 104: Water Closets (604)
grab bars clearances (609.3) further determine location of non-recessed dispensers

## Slide 105: Water Closets (604)
large dispensers can conflict with grab bar clearance

## Slide 106: Toilet Compartments (604)
compartments with > 1 fixture to meet room requirements
removed alternate stall designs (technical infeasibility)

## Slide 107: Wheelchair Compartments (604)
Standard Stall
60” min. wide
depth:
56” min. (wall hung toilet)
59” min. (floor-mounted or children’s toilet)

## Slide 108: Ambulatory Accessible Stalls (604)
depth specified (60” min.)
width: 35”- 37” (instead of 36” absolute)

## Slide 109: Urinals (605)
minimum depth specified
17” max rim height
* Accessibility only required if more than one urinal is provided

## Slide 110: Lavatories & Sinks (606)
apron clearance (29” min.) removed
parallel approach - kitchen sinks in spaces without cook tops/ conventional ranges
removable cabinetry - sinks & lavs in dwelling units (if certain conditions met)

## Slide 111: Bathtubs & Shower Compartments (607& 608)
hand-held shower spray (on/off control)
water temperature (120 degrees max.)
grab bars – can be adaptable in private bathrooms & dwelling units bathrooms

## Slide 112: Bathtubs (607)
additional 12” clearance beyond permanent seat

## Slide 113: Shower Compartments (608)
Alternate design permitted in any facility

## Slide 114: Figure 608.2.1 Transfer Type Shower Compartment Size and Clearance

## Slide 115: Figure 608.2.2 Standard Roll-In Type Shower Compartment Size and Clearance

## Slide 116: Grab Bars (609)
wider diameter – 2” max. (instead of 1 ½”)
circular and non-circular cross sections
(4” – 4.8” perimeter dimension; 2 ” max. cross section dimension)

## Slide 117: Grab Bars (609)

## Slide 118: Grab Bars (609)
12” min. clearance above
1 ½” min. below

## Slide 119: Grab Bars
609.4 Position of Grab Bars. Grab bars shall be installed in a horizontal position, 33 inches (840 mm) minimum and 36 inches (915 mm) maximum above the finish floor measured to the top of the gripping surface

## Slide 120: Saunas & Steam Rooms (612)
from supplement on recreation facilities
bench
turning space

## Slide 121: Communication Elements & Features (Chapter 7)
Fire Alarm Systems
Signs
Telephones
Detectable Warnings
Assistive Listening Systems
ATMs & Fare Machines
Two-Way Communication Systems

## Slide 122: Fire Alarm Systems (215)
public and common use areas
employee work areas (wiring)
transient lodging
residential facilities
alterations: compliance required where system upgraded or replaced or a new one is installed

## Slide 123: Fire Alarm Systems (702)
NFPA 72
(1999 or 2002)
guidelines require
110 dB max.

## Slide 124: Visual Alarms (702)
NFPA 72 covers:
flash rate & pulse duration
location - wall & ceiling
minimum intensity
(based on coverage area)
larger coverage thru fewer appliances
many spaces (other than corridors) can be covered by 1 appliance
synchronization of multiple appliances

## Slide 125: Signs (216)
Specific provisions for:
Means of egress
  Exit doors: Visual and Tactile (703.1, .2, & .5)
    Plus Braille for Raised Characters (703.3)
  Areas of Refuge (instructions and directions to): Visual (703.5)

## Slide 126: Signs (216)
Specific provisions for:
Parking
  Signage at spaces comply with 502.6
  Where a total of four or fewer parking spaces, including accessible spaces, are provided on a site, parking signage shall not be required.
  In residential facilities, where parking spaces are assigned to specific residential dwelling units, parking signage shall not be required

## Slide 127: Signs (216)
Specific provisions for:
Entrances
  Where not all entrances comply with 404, entrances complying with 404 shall be identified by the International Symbol of Accessibility complying with 703.7.2.1.
  Directional signs complying with 703.5 that indicate the location of the nearest entrance complying with 404 shall be provided at entrances that do not comply with 404.

## Slide 128: Signs (216)
Specific provisions for:
Toilet and bathing rooms
  Where existing toilet rooms or bathing rooms do not comply with 603, directional signs indicating the location of the nearest toilet room or bathing room complying with 603 within the facility shall be provided.
  Directional signs shall comply with 703.5 and shall include the International Symbol of Accessibility complying with 703.7.2.1.

## Slide 129: Signs (216)
Specific provisions for:
Toilet and bathing rooms
      Where existing toilet rooms or bathing rooms do not comply with 603, the toilet rooms or bathing rooms complying with 603 shall be identified by the International Symbol of Accessibility complying with 703.7.2.1.
      Where clustered single user toilet rooms or bathing facilities are permitted to use exceptions to 213.2, toilet rooms or bathing facilities complying with 603 shall be identified by the International Symbol of Accessibility complying with 703.7.2.1 unless all toilet rooms and bathing facilities comply with 603.

## Slide 130: Tactile Signs (703)

## Slide 131: Detectable Warnings
Where required:
Transit platforms (8.10.5)
Curb ramps at transit facilities (DOT rule) – bottom 2’
Public streets & sidewalks – recommend use of draft ROW guidelines

## Slide 132: Detectable Warnings (705)
greater range of designs & products allowed
dome diameter (range)
spacing (range)
removed:
resiliency/ sound-on-cane contact
color contrast

## Slide 133: ATMs & Fare Machines (220 & 707)
Access to 1 of each type at each location
speech output
privacy
input controls
display screen
Braille instructions (for speech mode)

## Slide 134: Special Rooms, Spaces & Elements (Chapter 8)
Assembly areas
Dressing, fitting, and locker rooms
Kitchens and kitchenettes
Medical care and long-term care
Transient lodging
Prison cells
Courtrooms
Dwelling units
Transportation facilities
Storage

## Slide 135: Assembly Areas (221)
Wheelchair Spaces
lower scoping for
assembly areas with
more than 500 seats:
501 – 5,000 seats: 1 space/ every 150 seats (instead of 1%)
> 5,000: 0.5% scoping

## Slide 136: Scoping: Assembly Areas

## Slide 137: Assembly Areas (221)
Dispersion of wheelchair
spaces to provide
choices of seating
locations and viewing angles
substantially equal to, or better than,
the choices of all other spectators

## Slide 138: Assembly Areas (221)
Exceptions for areas with 300 or fewer seats if:
horizontal – spaces & companion seats located in the 2nd or 3rd quartile of row
vertical – if viewing angles = or better than the average viewing angles in the assembly area

## Slide 139: Wheelchair Spaces (802)
Lines of Sight
Seated Spectators
  Over heads
  Between heads
Standing Spectators
  Over heads
  Between heads

## Slide 140: Wheelchair Spaces (802)
Circulation paths cannot overlap wheelchair spaces

## Slide 141: Assembly Areas (221)
Other Changes:
Companion seat
for each space
(can be movable)
Designated aisle seats - 5% of aisle seats
Lawn seating - accessible route

## Slide 142: Companion Seats and Designated Aisle Seats (802)
Companion Seats
  Alignment
  Type
Designated Aisle Seats
  Armrest
  Identification
1:48

## Slide 143: Dressing, Fitting, & Locker Rooms (222)
Access to at least 5% of each type of use in each cluster
(no change from original ADAAG)

## Slide 144: Dressing … & Locker Rooms (803)
Door swing into turning space (if wheelchair space beyond swing)
A bench complying with 903 is required

## Slide 145: Holding and Housing Cells Judicial (231) Detention/Correctional (232)
Judicial Facility
Central Holding
Court-Floor Holding
Detention/Correctional
General Holding/Housing
  - Mobility 3%*
  - Comms. 2%
Special and Medical
Visiting Areas Alterations
*as per DOJ regulation

## Slide 146: Holding and Housing Cells (807)
Mobility Features
- turning space
- benches
- beds
- toilet and bathing
Communication Features
- alarms
- telephones

## Slide 147: Courtrooms Judicial Facilities (231.2)
Scoping
Each court room
Technical (808)
turning space
clear floor spaces
counters/tables

## Slide 148: Transportation Facilities (218)
Scoping (each)
Rail stations
Bus shelters
Other
  public address systems
  clocks

## Slide 149: Transportation Facilities (810)
Bus Boarding Area
Surface
Dimensions
Connection
Slope
Shelters
Bus Signs

## Slide 150: Built-In Elements (Chapter 9)
Dining & Work Surfaces
Benches
Check-Out Aisles & Service Counters

## Slide 151: Dining & Work Surfaces (226)
Access to at least 5%, not fewer than 1
[no change from UFAS and original ADAAG]

## Slide 152: Sales & Service (227 and 904.4)
227 Scoping
Counters – 1 of each type
Cash register not factor
904.4 Technical
Accessible part same depth
Parallel or forward approach
No alternatives
Exception for alterations
Security glazing – voice communication

## Slide 153: Work Surface (902) Service Counter (904)
34” max
36” max
34” max
36” max

## Slide 154: [changing] Benches (903)
clear floor space (parallel-short axis
Size: (42” min. long, 20” – 24” deep)

## Slide 155: Recreation Facilities (Chapter 10)

## Slide 156: Sports Facilities
Area of sport activity defined as:
“That portion of a room or space where the play or practice of sport occurs”
Accessible route to each “area of sport activity”
Exempt from firm, stable, and slip resistant surface provision (302.1 EX2)

## Slide 157: Exercise Equipment and Machines

## Slide 158: Team player seating areas
Team player seating areas
  Platform lift permitted

## Slide 159: Area of sport activity
Court Sports -
Accessible route to directly connect both sides of the court

## Slide 160: Accessible route connecting various elements of a multi-use facility

## Slide 161: Accessibility not required to or in:
Raised boxing or wrestling rings
Raised structures solely for refereeing, judging, or scoring a sport.

## Slide 162: Fishing piers and platforms
Accessible routes serving floating piers/platforms – use boating gangway exceptions
Design gangway to 1:12 OR provide up to a 30 foot gangway
At least 25 percent of the railings, guards, or handrails shall be 34 inches (865 mm) maximum above the ground or deck surface.

## Slide 163: Fishing piers and platforms
Railings
  Where provided
  Maximum 34 inch height for 25% of the railing
  Lowered railing dispersed
  Exception: where a guard is provided which complies with ICC/IBC

## Slide 164: Fishing piers and platforms
Edge protection – where railings are provided – 2 inch minimum
30 inches x 48 inches clear space
At least one maneuvering space

## Slide 165: Play Areas (240 and 1008)
Contains play components
Designed and constructed for children
Separated by age ranges for safety

## Slide 166: What is a Play Component?
A play component is an element designed to generate specific opportunities for play, socialization, and learning.

## Slide 167: Ground-Level Requirements
“One of Each Type”
More than one — integrated in the play area
Ground-Level requirements based on number of Elevated Play Components

## Slide 168: Minimum Number of Elevated Components
50% of all elevated play components in a play area must be reached by an accessible route
20 or more elevated components:
25 % ramp + 25% ramp and/or transfer = 50%
Less than 20 elevated components:
ramp and/or transfer = 50%

## Slide 169: Based on the number of elevated play components provided, and using the table
Minimum quantity of
ground-level play
components
Minimum number of
different types
Number and Types of Ground Level Play Components Required to be on Accessible Route
5
8 plus 1 for each additional 3 over 25, or fraction thereof
More than 25
4
8
23 to 25
4
7
20 to 22
3
6
17 to 19
3
5
14 to 16
3
4
11 to 13
3
3
8 to 10
2
2
5 to 7
1
1
2 to 4
Not applicable
Not applicable
1
Minimum Number of Different Types of Ground Level Play Components Required to be on Accessible Route
Minimum Number of Ground Level Play Components Required to be on Accessible Route
Number of Elevated Play Components Provided

## Slide 170: Swimming pools
Required means of access into the water
  Over 300 linear ft of pool wall = 2
  Less than 300 linear ft of pool wall = 1
Lift or sloped entry
Second means - lift, sloped entry, transfer wall, stairs, or transfer system

## Slide 171: Sloped Entry
Extend to 24 inches to 30 inches below stationary water level
1:12 maximum slope
Handrails – 33 inches – 38 inches clear width

## Slide 172: Pool lift
Located where water does not exceed 48 inches
Footrests – must be provided and move with seat.
Armrest – if provided opposite water shall be removable or fold in raised or load position
Capable of unassisted operation – both deck and water

## Slide 173: Other means of access into the water

## Slide 174: Wading pools
At least one sloped entry – handrails not required
Extend to the deepest part of the wading pool

## Slide 175: Water play components
Where water play components are provided, ground level access and transfer access to elevated play components required

## Slide 176: Accessibility not required to or on:
Water slides
Accessible route required to edge of catch pool

## Slide 177: Saunas and Steam Rooms
Where provided in a cluster, at least 5%, not less than one
Turning space within the room—may be obstructed by readily removable seats
Door swing can not swing into clear floor/ground space for bench

## Slide 178: Resources
ACTCP- Great Plains ADA Center
100 Corporate Lake Dr
Columbia, Mo 65203
573-882-3617
Southwest ADA Center
TIRR Memorial Hermann - ILRU
1333 Moursund
Houston, TX 77030
800-949-4232 or 713-797-7171.