## Slide 1
Accessible
Pedestrian Facilities in the
Public Right-of-Way
Presented By: Michael Edwards Great Plains ADA Center
Slides by
Melissa Anderson, PE
Principal, Melissa A Anderson, LLC

## Slide 2: Agenda
Legal Obligations for Accessibility
Organization of Proposed Rule
Pedestrian Access Route
Pedestrian Circulation Area
Curb Ramps and Blended Transitions
Pedestrian Crossings
Transit Stops and Shelters
Parking
Questions and Answers

## Slide 3: Pedestrians with Disabilities
Pictures of persons with different disabilities

## Slide 4: Discrimination is Illegal
1973 Rehabilitation Act, Section 504
- Prohibits discrimination based on disabilities
- Applies to programs and activities receiving Federal funds
1990 Americans with Disabilities Act
  - Civil Rights Law
  - Prohibits discrimination in the provision
  of facilities, services, and programs
- Title II applies to State and Local Governments

## Slide 5
Established in 1973 as an independent Federal agency
Tasked with developing design criteria and providing technical assistance to ensure access
  Built environment – buildings, sites and infrastructure
  Transportation vehicles
  Telecommunication and information technology
Adoption and enforcement responsibilities belong to other
agencies
  Department of Justice
  Department of Transportation
  and others
The Access Board is responsible for enforcing the Architectural Barriers Act in facilities built
with Federal funds
United States Access Board
5

## Slide 6: Standards vs. Guidelines
Guidelines are developed by the Access Board but must be adopted by another responsible agency to become enforceable standards.
Current enforceable standard is ADAAG or 2010 ADA Standards
FHWA Memo 1/23/06
  - PROWAG – “recommended best practices, and can be considered the state of the practice that could be followed for areas not fully addressed by the present ADAAG standards”
6

## Slide 7: Rulemaking Update
Final Rule Draft approval by the Access Board
Review by the Office of Management and Budget
Publication in the Federal Register
Adoption by the Department of Justice and Department of Transportation
Graphic image of a rocker switch
Graphic image showing high and low unobstructed reach range (48 inches above finished floor or ground maximum and 15 inches above finished floor or ground minimum)

## Slide 8: Supplemental Notice of Proposed Rulemaking Accessibility Guidelines for Pedestrian Facilities in the Public Right-of-Way; Shared Use Paths (2013)
Incorporates shared use path guidelines into the 2011 proposed PROWAG (web only)
  R1 Application and Administration
  R2 Scoping Requirements
  R3 Technical Requirements
  R4 Supplementary Technical Requirements

## Slide 9: What can State and Local Agencies do in the meantime?
Policy
Standards
Education
Enforcement at local level

## Slide 10: Accessibility Obligations
New construction is required to be accessible
Alterations to existing facilities must be accessible to the maximum extent practicable
            Existing facilities that have not been altered can not deny access to persons with disabilities
10

## Slide 11: Technical Requirements Pedestrian Access Route

## Slide 12: Sidewalks - Who needs them?
12
If sidewalks are provided, then they are required to be accessible to and usable by a person with a disability.

## Slide 13: Types of Pedestrian Facilities Pedestrian Access Routes
Sidewalks
(pedestrians only)
Shared-use Paths
(peds and bikes)
Shoulders
13

## Slide 14: Pedestrian Access Route Basics
Contains 48” min pedestrian access route, (36” min accessible route);
2% maximum cross slope;
Surface is firm, stable and slip resistant;
Minimize level changes;
No protruding objects within circulation path;
Clear floor space at entrances, pedestrian pushbuttons, and other pedestrian features (drinking fountains, telephones, ATMs…)
14

## Slide 15: Pedestrian Access Route Clear Width
4 ft min clear width exclusive of the curb with a 5 ft passing space every 200 ft max
Photo of wide side walk with 2 brick strips with an arrow in the middle depicting the four foot requirement
4 ft min

## Slide 16: Shared Use Path Width
Width determined by use and not accessibility
16

## Slide 17: Clear Width
48” min clear width continues around all obstructions
17

## Slide 18
Which one meets the requirements??
18

## Slide 19: Pedestrian Access Route Running Slope
R302.5.1 Within Street or Highway Right-of-Way. Except as provided in R302.5.3, the grade of pedestrian access routes shall not exceed the general grade established for the adjacent street or highway.
R302.5.2 Not Within Street or Highway Right-of-Way. The grade of pedestrian access routes shall be 5 percent maximum.
R302.5.3 Within Pedestrian Street Crossings. The
grade of pedestrian access routes shall be
5 percent maximum.
Photo of steep urban roadway with a curb attached sidewalk

## Slide 20: Accessible Route Running Slope
What it looks like if the building guidelines are applied
Photo of sidewalk with a switchback ramp on it with handrails

## Slide 21: Pedestrian Access Route Cross Slope
0% best for wheelchair users
Some slope needed for drainage
Max cross slope 2%
Graphic showing cross slope of 2% in the middle with steeper cross slope on each side

## Slide 22: Pedestrian Access Route Cross Slope
Photo of construction worker measuring cross slope with a level before concrete is poured
Photo of an existing sidewalk with the middle at a 2% cross slope; with a steeper cross slope near the building
2% HERE
Cross Slope: 2% maximum
Construction tolerances?
Design accordingly – 1.5%?

## Slide 23: Driveways
Design a continuous usable cross slope
23

## Slide 24: Pedestrian Access Route Surface
Surfaces: stable, firm and slip resistant
Photo of sidewalk with grass on each side and large trees

## Slide 25
Properly installed, and well maintained bricks and pavers can work. Beveled edges are a problem for rollability.
Surfaces
25

## Slide 26: Surfaces Shared Use Paths and Trails
Loose surface materials:
Generally need special treatment (e.g., binders, consolidates, compaction, and grid forms)
Frequent maintenance
NCA’s website - http://www.ncaonline.org/
loose gavel surface material
National Trails Surface Study

## Slide 27: Surface Discontinuity
27
* Grade breaks must be flush – curb ramps!

## Slide 28: Pedestrian Access Route Surface
Horizontal openings no more than ½ inch in the direction of travel
Photo of wheelchair caster going over a grate that has bars welded on it to make the openings smaller
Photo of wheelchair caster stuck in elongated openings of grate

## Slide 29: Temporary Pedestrian Access Routes
Must have access to temporary events and facilities –
  Farmers markets
  Food trucks, etc.
Maintenance of accessible
facilities -
  Construction detours

## Slide 30: Alternate Pedestrian Access Route in Work Zones
Image of pedestrian routes around construction
Image of cane detectable barrier around construction materials on a sidewalk

## Slide 31: Curb Ramps and Blended Transitions

## Slide 32: Curb Ramps & Blended Transitions
One ramp for each street crossing
Image of an intersection with diagonal curb ramps showing the preferred straight line of pedestrians and the zigzag route required by using the curb ramps provided
Notes: 32

## Slide 33: Anatomy of a Curb Ramp
The ‘cookie cutter’ curb ramp
Turning Space
Running slope - 8% max*
Cross slope - 2% max*
Counter slope - 13% max
Flare slope - 10% max
Turning space*
Perpendicular grade breaks
Flush transitions

## Slide 34: Perpendicular Curb Ramps
Ramp slope perpendicular to the curb or street crossing
Graphic of 2 perpendicular curb ramps at a corner
Image of perpendicular curb ramp

## Slide 35
Turning space is required at the top of curb ramps for changing direction (4’ x 4’ min, 4’x 5’ if constrained)
Perpendicular Curb Ramps

## Slide 36: Parallel Curb Ramps
Ramp slope parallel to the curb or street crossing
Graphic of parallel curb ramp
Image of parallel curb ramp

## Slide 37: Blended Transitions
Blended Transition (depressed corner)
Graphic of a blended transition
Image of blended transition a depressed corner
2% cross slope to travel around the corner

## Slide 38: Blended Transitions
Blended Transition (raised crossing)
Graphic of a blended transition
Image of a blended transition a raised crossing

## Slide 39: Combination Curb Ramps
Combination ramp
Graphic of a combination curb ramp
Image of a combination curb ramp

## Slide 40
Counter
Slope
40
Counter slope 5% max.

## Slide 41: Detectable Warning Devices

## Slide 42: Detectable Warning Devices
Image of blended transition with detectable warnings
Image of curb ramps with detectable warnings
Image of curb ramp with detectable warnings

## Slide 43: Detectable Warning Devices (FHWA Memo)
Provide warning to the visually impaired that they
are about to enter a hazardous area.
Required at all street crossings, transit boarding platforms - driveways??
Raised domes with in-line or
radial arrangement
24” min. and full width
of curb ramp
Contrasting in color

## Slide 44: Detectable Warning Devices
Detectable warning depth and width? Contrast with surrounding surface required
Five images showing detectable warning placements

## Slide 45: Detectable Warning Devices
Due to their distinctive design, truncated domes are detectable by cane and underfoot
Figure R305.1.2 Dome Spacing: Truncated domes in plan view with a center-to-center spacing of 41 mm (1.6 in) min and 61 mm (2.4 in) max, and a base-to-base spacing of 17 mm (0.65 in) min, measured between the most adjacent domes
Figure R305.1.1 Dome Size: Truncated dome in elevation shown with a base diameter of 23 mm (0.9 in) min to 36 mm (1.4 in) max, a top diameter 50% to 65% of the base diameter, and a height of 5 mm (0.2 in)

## Slide 46
DW placement on parallel curb ramp
Detectable Warning Location
24”
Place at back of curb on landing
46

## Slide 47: Detectable Warning Location
Pedestrian refuge islands
A photo of a pedestrian refuge island with detectable warnings

## Slide 48: Pedestrian Crossings

## Slide 49: Street Crossings
49

## Slide 50: Pedestrian Street Crossings
Continuation of PAR
Walking speed – 3.5 ft/sec
Image of several able bodied people crowded onto the curb ramp waiting to cross
Image of a pedestrian using a walker crossing a street

## Slide 51: Street Crossings
5% max running slope, or street crown (PROWAG only);
2% max cross slope on curb ramps and crosswalks, exception for some intersections;
Pedestrian walk indicators with non-visual information provided (Accessible Pedestrian Signal);
Adequate crossing time (3.5 fps);
Multi-lane roundabouts need some type of pedestrian demand signalization.
51

## Slide 52
Crosswalks
MUTCD provides definition of a crosswalk

## Slide 53: Pedestrian Crosswalks
The guidelines do not tell you when to mark
Or how to mark (look at MUTCD part 3)
Image of a marked crossing
Image of a marked crossing

## Slide 54: Pedestrian Crosswalk Cross Slopes
Image of steep street that has been leveled off at the intersection
Maximum crosswalk cross slope
2% is a general requirement for pedestrian access routes
5% is allowed in a street crossing without stop or yield vehicle control – free flow (PROWAG only)

## Slide 55
Pedestrian Crosswalks at Roundabouts
Pedestrian crossing easily located for way finding at all roundabouts – separation from circulatory lanes
Where pedestrian crossings are multi-lane; pedestrian-activated signals shall be provided
Image of separated sidewalk at roundabout with a pedestrian signal and image of fence around circulatory roadway at roundabout

## Slide 56: Accessible Pedestrian Signals (APS)

## Slide 57: Accessible Pedestrian Signals – www.apsguide.org
57

## Slide 58: Accessible Pedestrian Signals
Button
- Face of button parallel to crosswalk
- Mounted at 42” (48” max used to be 54”)
- Max. 5 lbs pressure needed to activate
Sign
- Adjacent to button – explains
purpose and use
- Must clearly indicate crosswalk
direction
58

## Slide 59
Pedestrian Push Button Location
- Accessible route to ramp
and crossing
- Reachable (10 in) from a clear space
- 5 ft from the crosswalk
- 1.5-6 ft from edge of curb
or pavement
- See MUTCD Guidance Fig. 4E-4
59

## Slide 60: Pedestrian Push Button Location
60
Find the pushbutton. Now line up to cross.
Missed your chance? Do it again
A wide sidewalk with the pedestrian pushbutton as far from the crossing as would be possible

## Slide 61: Accessible Pedestrian Signals Reach Ranges from Clear Space
61
Vertical
Max. Reach – 48”
Min. Reach – 15”
(forward & side)
Horizontal
Side reach within 10”
Forward reach – no obstruction or space

## Slide 62: Accessible Pedestrian Signals
Accessible Features MUTCD 4E.08-4E.13
- Locator tone
- 10 ft. separation, or speech indication
- Speech walk criteria MUTCD 4E.11
- Volume adjusts for ambient noise
- Extended Press Features
- Tactile arrow indicates direction
62

## Slide 63: Accessible Pedestrian Signals
Three images of pedestrian push button,2 examples of large pedestrian push button with tactile arrow; and one pedestrian with guide dog using APS;

## Slide 64: On-Street Parking

## Slide 65: On-Street Parking Scoping
Number of accessible spaces is based upon total on a block perimeter
Scoping Section R214
No van parking required
Image of On-Street parking Permits Zone showing several blocks in downtown Tampa FL

## Slide 66: On-Street Parking in a Wide ROW
Where the width of the adjacent sidewalk or available right-of-way exceeds 14 ft. an access aisle is required
A 1.5 m (5 ft) wide min access aisle running the full length of parallel parking space and located beyond the face of curb at sidewalk at least 4.3 m (14 ft) wide; aisle served by curb ramp at one end
Image of parallel parking with access aisle

## Slide 67: On-Street Parking in a Narrow ROW
Narrow sidewalks – an access aisle is not required
A photo of on-street parking. Several "accessible" spaces include the wheelchair symbol on the payment. Signs are also provided.
In this case, the on-street spaces are located on a narrow sidewalk but not closest to the corner crosswalk. A figure showing on street parking where there are narrow sidewalks. The space is located at the end of the block closest to the curb ramp at the crossing. l

## Slide 68: On-Street Parking
Angled (or perpendicular) on-street parking
Image of angled parking with an access aisle
Graphic of accessible angled parking

## Slide 69: On-Street Parking Displays and Information
Information must be visible from a point 3.3 ft. max above the center of the clear space
Meet operable parts requirements
Located at the head or foot of space
A photo of on-street parking. Several "accessible" spaces include the wheelchair symbol on the payment. Signs are also provided.
In this case, the on-street spaces are located on a narrow sidewalk but not closest to the corner crosswalk. A figure showing on street parking where there are narrow sidewalks. The space is located at the end of the block closest to the curb ramp at the crossing. l

## Slide 70: Documents Available Online
www.access-board.gov
SNPRM for Proposed Guidelines for Public Rights-of-Way
Accessible Public Rights-of-Way: Planning and Designing for Alterations
Accessible Sidewalks (DVD, or download)
Detectable Warnings Update
Manufacturers of Detectable Warning Products
As well as many research reports

## Slide 71: Questions? Access Board www.access-board.gov Email – row@access-board.gov Technical Assistance – 800-872-2253 Southwest ADA Center 800-949-4232 www.southwestada.org Melissa Anderson, PE Anderson@Engineering4Access.com
Image of street sign reading caution pedestrians slippery when wet with a 2 hour parking sign below